## Slide 1: Tethered 6U CubeSat
Tether range, relative attitude, heritage and 3D imaging
CUBICS 2026 · Stream 1 · Team meeting, October 2026
Notes: Goal of the meeting: agree on tether length, attitude sensors and the imaging claim before writing the proposal. All numbers assume two 4 kg halves at 550 km.

## Slide 2: Four answers for today
SUMMARY
Tether range
Vertical only. 500 m to 1 km is feasible: 3.6 to 7.2 mN of tension and about 3.5 h to deploy.
Relative attitude
IMUs alone drift within minutes. Add a star tracker on each half and dual GNSS; use the stowed zero only to calibrate.
State of the art
Tethers have flown since 1966. Most failures happen during deployment.
3D photos
Not with a 0.5 to 1 km baseline: errors of 0.8 to 1.7 km. Yes with fore/aft camera pointing: about 3.5 m.
Notes: One card per question raised for this meeting. The rest of the deck backs each card with numbers.

## Slide 3: Only a vertical tether stays taut
1 · TETHER RANGE AND ORIENTATION
Gravity pulls the lower half a little more and the upper half a little less.
That difference keeps the three tethers taut, with no power.
The pair settles along the local vertical by itself.
T = 3 n² m_eq L
n = orbital rate at 550 km, m_eq = 2 kg, L = separation. Tension grows linearly with the tether length.
Notes: Gravity gradient: below the orbit centre gravity exceeds what circular motion needs, above it falls short. The tether supplies the difference. This only works radially; along-track gives zero tension and cross-track pushes the halves together.

## Slide 4: 500 m to 1 km: the key numbers
1 · TETHER RANGE AND ORIENTATION
Quantity | L = 500 m | L = 1 km
Total tension | 3.6 mN | 7.2 mN
Tension per tether (3 tethers) | 1.2 mN | 2.4 mN
Deployment time, controlled | 3.2 h | 3.5 h
Free deployment, no brake | 75 min, ends at 0.95 m/s | 81 min, ends at 1.9 m/s
Tether mass (3 × 0.2 mm) | 66 g | 132 g
Elastic stretch at full tension | 0.2 mm | 0.8 mm
Thermal length change (±100 K) | 0.15 to 0.5 m | 0.3 to 1.0 m
Tether frontal area (drag) | 0.30 m² | 0.60 m²
Orbit life at 550 km, deployed | ≈ 1.2 years | ≈ 0.6 years
Two 4 kg halves, three 0.2 mm tethers, 550 km. Orbit life uses a simple drag model with mean solar activity; the formal analysis is still to do.
Notes: Controlled deployment: tether paid out exponentially at half the orbital rate, which keeps libration bounded. Orbit life: the tethers themselves add 0.3 to 0.6 square metres of drag area, more than the satellites. That shortens the mission but helps the 5-year deorbit rule.

## Slide 5: Slow deployment keeps the tether vertical
1 · TETHER RANGE AND ORIENTATION
3.2–3.5 h
controlled deployment to 500 m or 1 km
< 30°
libration during a controlled deployment
1.9 m/s
end speed of a free 1 km deployment: the tether tumbles
Notes: The winch pays the tether out slowly. Too fast and the Coriolis effect tips the tether towards horizontal. The free curve is the textbook cosh solution, which ignores libration.

## Slide 6: A diagonal tether cannot be held
1 · TETHER RANGE AND ORIENTATION
Gravity always pulls the pair back to vertical; a tilt becomes a 55-minute swing.
Holding 30° at 1 km would need 3.1 N·m, about 3,000 times a reaction wheel.
A tilted tether also carries less tension: cos² of the angle.
Diagonal is a swing, not a configuration
Notes: Static tension at angle phi is 3 n^2 m_eq L cos^2 phi, and the gravity-gradient torque 3 n^2 I sin phi cos phi always pushes back to vertical. Only wheels could hold the angle and they are three orders of magnitude too weak.

## Slide 7: Once deployed, the length stays fixed
1 · TETHER RANGE AND ORIENTATION
The winch sets the length. More tension does not lengthen the tether; it only pulls it tighter.
< 1 mm
elastic stretch at full tension, even at 1 km
up to 1 m
length change between sun and shadow: the winch must compensate
55 min
period of the natural swing around vertical
Paying out faster only adds swing and braking load; it does not give a longer or tighter tether.
Notes: Answer to the idea that the tether keeps separating as speed or tension grows: tension rises linearly with length (3.6 mN at 500 m, 7.2 mN at 1 km) but the stretch is below a millimetre. The real length change is thermal, up to a metre at 1 km for polyethylene fibre, which is why active winch compensation matters.

## Slide 8: IMUs alone lose the zero within minutes
2 · RELATIVE ATTITUDE
Gyros measure rotation rate, so small errors add up over time.
A good 1°/h MEMS gyro is off by 1.6° after one orbit.
Accelerometers cannot sense attitude in free fall.
Mapping images needs 0.01 to 0.05°: only an absolute sensor holds that.
Notes: Setting both IMUs to zero while the halves are joined is a good calibration step, but it does not survive. The error grows with time and cannot be reset without an external reference.

## Slide 9: Recommended sensors for relative attitude
2 · RELATIVE ATTITUDE
Star tracker on each half
Absolute attitude of each half to about 0.005°, at any time.
GNSS receiver on each half
Relative position at centimetre level: tether direction to about 0.001° at 1 km.
Tether direction encoders
Angle of the tether at each anchor, measured directly.
IMU
Fast rates between updates and during manoeuvres.
Stowed zero: use the joined state to calibrate the mounting offset between both halves, not as the reference for the whole mission.
Notes: Relative attitude = attitude of B minus attitude of A, each from its own star tracker. Dual GNSS gives the baseline vector, i.e. the tether direction. Encoders give a third, independent check.

## Slide 10: Tether heritage: deployment is the main risk
3 · STATE OF THE ART
Mission | Year | Length | What happened
Gemini XI | 1966 | 30 m | First tether test between two spacecraft
SEDS-1 | 1993 | 20 km | Full deployment; end mass deorbited
SEDS-2 | 1994 | 19.7 km | Closed-loop braking law validated
TSS-1R | 1996 | 19.7 km | Tether broke by an electrical arc
TiPS | 1996 | 4 km | Libration damped from 40° to 7.5°
ATEx | 1999 | 22 m of 6.2 km | Tether went slack after a thermal transient
YES2 | 2007 | 31.7 km | Longest structure deployed in orbit
TEPCE | 2019 | 1 km | Two CubeSat halves split by a stacer spring at 4 m/s
Notes: Failures cluster in deployment: friction, slack and electrical issues. ATEx is the closest warning for us: the tether went slack after sunrise. TEPCE is the closest architecture: a CubeSat split in two by a spring.

## Slide 11: Previous tethered systems
3 · STATE OF THE ART
Two CubeSats joined by a tether
Two end bodies joined by a tether with a three-line bridle
Tether between a spacecraft and a target body
Momentum-exchange tether: catch and toss of a payload
Notes: Images provided by the team from previous tether work. Confirm the original mission and source of each image before citing them in the proposal.

## Slide 12: Where our proposal fits
3 · STATE OF THE ART
Already demonstrated
Splitting a CubeSat in two with a spring (TEPCE, 2019)
Kilometre-class deployment with braking (SEDS-2, TiPS)
Gravity-gradient stabilisation along the vertical
Libration damping with the winch
New in this proposal
Three tethers between the same two bodies
Active thermal compensation of length (the ATEx failure)
Tether direction measured at the anchors
Earth imaging from both halves
Notes: The novelty is not deploying a tether, which is well proven, but controlling three tethers and their thermal length change at CubeSat scale.

## Slide 13: 3D needs two very different viewing angles
4 · 3D IMAGING
Notes: Height comes from parallax: how much a summit shifts between two photos. The shift is proportional to the baseline divided by the altitude, B/H.

## Slide 14: A 0.5–1 km baseline gives errors near 1 km
4 · 3D IMAGING
825 m
height error with a 1 km baseline, 5 m pixels
1.65 km
height error with a 500 m baseline
0.36 px
shift of a 1 km-high mountain between the two photos
And a vertical tether gives no stereo at all: both cameras look along the same line.
Notes: Height error = matching error / (B/H). With 0.3 pixel matching at 5 m pixels, that is 1.5 m divided by B/H. Even a horizontal 1 km baseline gives B/H = 0.0018. Relief needs at least about 8 km of baseline for 100 m error.

## Slide 15: What works: pointing the cameras
4 · 3D IMAGING
Option | B/H | Height error 5 m / 20 m px | Notes
Fixed fore/aft cameras (A +12°, B −12°) | 0.43 | 3.5 m / 14 m | Simple; sites under the track
Gimbal ±30° on each half | 0.40 | 3.8 m / 15 m | Chosen sites; 2 to 4 day revisit
Tether baseline, 1 km | 0.0018 | 825 m / 3.3 km | Not usable
Simulator: both halves image the same hill 31 s apart
The 3D comes from the satellite moving along its orbit, not from the tether.
Notes: Fore/aft: half A looks 12 degrees ahead, half B 12 degrees behind; 234 km of orbit between shots. The gimbal adds 635 km of reachable swath. Present 3D as a secondary objective; the tether's value is thermal compensation and metrology.

## Slide 16: Going to 1 km adds new risks
5 · RISKS AND NEXT STEPS
Drag
Tethers add 0.6 m² of drag area. Orbit life at 550 km falls to about 0.6 years.
Thermal
Up to 1 m of length change per orbit. The winch needs that range and control.
Debris
A 1 km object has a larger collision cross-section. Confirm admissibility with CSA.
Mass
132 g of tether and larger drums inside two 3U halves.
Notes: The drag point is the surprise: at 1 km the tethers dominate the drag. That helps deorbit compliance but may make the mission shorter than the operations plan. Run a formal lifetime analysis with STELA or DRAMA.

## Slide 17: Decisions for the team
5 · RISKS AND NEXT STEPS
1
Tether length
500 m or 1 km, weighed against mission life (1.2 vs 0.6 years at 550 km).
2
Attitude sensors
Star tracker and GNSS on each half; IMU and encoders as support.
3
Imaging claim
Drop tether stereo; use fore/aft or gimbal cameras for 3D.
4
Questions to CSA by 9 Nov
Launch altitude, tether admissibility, deorbit case.
5
Analysis
Formal orbit-life study and thermal model of the tether.
Notes: Close by agreeing owners and dates for each decision. Questions to CSA must go out before 9 November.